## Slide 1
Site-Specific Propagation Predictions of the Radio Channel Using NYURay Based on Measurements and Ray-Tracing at Upper Mid-Band Frequencies
Mingjun Ying
Advisor: Prof. Theodore S. Rappaport
M.S. Dissertation Defense
April 29, 2025
This research is supported by the NYU WIRELESS Industrial Affiliates Program.

## Slide 2: Agenda
3D Scene Reconstruction for Wireless Ray-Tracing
Conclusions and Future Work

## Slide 3
Conventional 3D Reconstruction
2.4 m
[1] Wireless EM Propagation Software | Wireless InSite® | Remcom
Indoor
Rural
Urban
Import AutoCAD 3D files (DXF) to different ray tracer.

## Slide 4: Conventional 3D Reconstruction: Indoor
[1] T. Rappaport and R. Skidmore, “Method and system for a building database manipulator,” U.S. Patent US20 050 131 619A1, Jun. 16, 2005. https://patents.google.com/patent/US20050131619A1

## Slide 5: Conventional 3D Reconstruction: Outdoor
2.4 m
[1] Blosm, https://prochitecture.com/blender-osm/extent/?blender_version=4.1&addon=blosm&addon_version=premium2.7.8
Blender Open Street Map (Blosm) add-on [1]
Pros:
Easy to generate.
Building shapes are generally accurate.
Material properties can be assigned easily.
Cons:
Some small objects are missing.
Few building roof shapes are wrong.
Detail of building exterior structure is missing.

## Slide 6: Site-Specific Outdoor UMi Environment
Lamp Post
Transformer
Concrete Pillars
Marble Pillars
Trees and Foliage
Stop Sign
Pedestrians
Bentch
Trash Bin
Fire Hydrant

## Slide 7: Conventional 3D Reconstruction: Outdoor
2.4 m
[1] https://prochitecture.com/blender-osm/extent/?blender_version=4.1&addon=blosm&addon_version=premium2.7.8
Manually Create Missing 3D Objects and Place Objects in Blender

## Slide 8
How Do We Unify 3D Reconstruction?
Main limitation of traditional methods
[1] T. Rappaport and R. Skidmore, Method and system for a building database manipulator, U.S. Patent 6,721,769, Apr. 13, 2004. https://patentimages.storage.googleapis.com/56/39/20/f1a9320fa181a0/US6721769B1.pdf
Time efficiency (manually create each object)
Low accuracy (small cabinets, ventilation tubes, trees, street lights, etc.)
No generalized and uniform database format [1]
What do we want?
Low cost
High efficiency
High accuracy
Generalized data format
Most promising solution:
Computer Vision
Material-Embedded 3D Scene Reconstruction

## Slide 9
Material-Embedded 3D Reconstruction
Modified Approach
Data Preparation

## Slide 10
2D Image Segmentation
Segmentation Anything 2 (SAM2)
[1] Nikhila Ravi, Valentin Gabeur, Yuan-Ting Hu, Ronghang Hu , Chaitanya Ryali, Tengyu Ma, Haitham Khedr, Roman R¨adle, Chloe Rolland, Laura Gustafson, et al. Sam 2: Segment anything in images and videos. arXiv:2408.00714, 2024. https://arxiv.org/abs/2408.00714

## Slide 11
Material Assignment
Performance of Different VLLM
Llama-3.2 11B Vision [1]
LLava v1.5 13B-4bit Vision [2]
ChatGPT-4 Vision [3]
Claude 3.5 Sonnet [4]
[1] Meta, "LLaMA 3.2: Vision edge for mobile devices," Meta AI, 2024. https://ai.meta.com/blog/llama-3-2-connect-2024-vision-edge-mobile-devices/
[2] K. Lee et al., "LLaVA v1.5 13B-4bit: Large vision-language model for detailed analysis," arXiv, 2023. https://arxiv.org/abs/2304.08485
[3] OpenAI, "GPT-4," OpenAI, 2024. [Online]. Available: https://openai.com/index/gpt-4/
[4] Anthropic, "Claude 3.5 Sonnet: Advanced multimodal language model," Anthropic, 2024. https://www.anthropic.com/news/claude-3-5-sonnet
All of them successfully identify the material as “itu_celling_board”,
but the small model (<7B parameters) performance is not satisfying,
need to train our own model for identifying material of different objects.

## Slide 12
Indoor 3D Environment Reconstruction
Modified Approach
Point Cloud Generation with Material Information Embedded.

## Slide 13
Material-Embedded 3D Point Cloud
[1] V. Leroy, Y. Cabon, and J. Revaud, "Grounding Image Matching in 3D with MASt3R," arXiv preprint arXiv:2406.09756, 2024. https://arxiv.org/abs/2406.09756
Material Information Embedded

## Slide 14
Indoor 3D Environment Reconstruction
Modified Approach

## Slide 15
Indoor 3D Environment Reconstruction
Raw Point Cloud
Processed Point Cloud
Open3D [1]
RANSAC [2]
Laplacian smoothing [3]
[1] Q.-Y. Zhou, J. Park, and V. Koltun, “Open3D: A modern library for 3D data processing,” arXiv preprint arXiv:1801.09847, 2018. https://arxiv.org/abs/1801.09847
[2] O. Chum, J. Matas, and J. Kittler, “Locally optimized RANSAC,” in Joint Pattern Recognition Symposium, Springer, 2003, pp. 236–243. https://link.springer.com/chapter/10.1007/978-3-540-45243-0_31
[3] D. A. Field, “Laplacian smoothing and Delaunay triangulations,” Commun. Appl. Numer. Methods, vol. 4, no. 6, pp. 709–712, 1988. https://onlinelibrary.wiley.com/doi/epdf/10.1002/cnm.1630040603

## Slide 16: Agenda
3D Scene Reconstruction for Wireless Ray-Tracing
Conclusions and Future Work

## Slide 17
Limitations of Current Methods
Impact on Ray Tracing Accuracy
  High sensitivity to mesh irregularities – Small errors can significantly distort ray paths
  Boundary artifacts (e.g., wall–floor junctions) reduce accuracy
  Missing geometry and holes in the 3D model affect completeness
  Inaccurate material identification weakens EM property assignment
  Inefficient computation in creating large-scale scenes
Consequence: Reduced accuracy in electromagnetic propagation predictions

## Slide 18
Potential Plan
For Outdoor Environment
  Creating object data base (common objects in the outdoor environment)
  UAV video/lidar scan for more accurate building shape reconstruction
For Indoor Environment
  Floor plan based efficient indoor reconstruction for less detailed 3D representation
  Video/Lidar scan aided detail enhancement
Guide for localization with outdoor base station

## Slide 19
Industrial Affiliates
This work is supported by the NYU WIRELESS Industrial Affiliates Program.

## Slide 20: References
[1] M. K. Samimi and T. S. Rappaport, “3-D millimeter-wave statistical channel model for 5G wireless system design,” IEEE Trans. on Microwave Theory and Techniques, vol. 64, no. 7, pp. 2207–2225, July 2016. https://ieeexplore.ieee.org/document/7501500
[2] S. Ju, Y. Xing, O. Kanhere and T. S. Rappaport, "Millimeter Wave and Sub-Terahertz Spatial Statistical Channel Model for an Indoor Office Building," in IEEE Journal on Selected Areas in Communications, vol. 39, no. 6, pp. 1561-1575, June 2021. https://ieeexplore.ieee.org/document/9411894
[3] Remcom, “Wireless InSite,” https://www.remcom.com/wireless-insite-em-propagation-software
[4] iBwave Solutions Inc., “ibwave design prediction accuracy,” 2025. https://www.ibwave.com/storage/app/media/pdf/white-papers/ibwave-design-prediction-accuracy%20white-paper.pdf
[5] EDX, Inc., “Software update release notes,” 2025. https://edx.com/software-update-release-notes/
[6] J. Hoydis, S. Cammerer, F. Ait Aoudia, M. Nimier‑David, L. Maggi, G. Marcus, A. Vem, and A. Keller, “Sionna,” 2022. https://nvlabs.github.io/sionna/
[7] Altair Engineering, Inc., “Altair winprop documentation,” 2025. https://help.altair.com/winprop/index.htm
[8] K. Guan, D. He, and Z. Zhong, “CloudRT: A Chinese example of open science infrastructure and services,” Cultures of Science, vol. 4, no. 4, pp. 217–226, 2021. https://journals.sagepub.com/doi/full/10.1177/20966083221084142
[9] O. Kanhere, H. Poddar and T. S. Rappaport, "Calibration of NYURay for Ray Tracing Using 28, 73, and 142 GHz Channel Measurements Conducted in Indoor, Outdoor, and Factory Scenarios," in IEEE Transactions on Antennas and Propagation, vol. 73, no. 1, pp. 405-420, Jan. 2025. https://ieeexplore.ieee.org/document/10721240
[10] S. Y. Tan and H. S. Tan, “A microcellular communications propagation model based on the uniform theory of diffraction and multiple image theory,” IEEE Trans. Antennas Propag., vol. 44, no. 10, pp. 1317–1326, Oct. 1996. https://ieeexplore.ieee.org/document/537325